SPECIFICATIONS

Mass of Aerosol Generating Solid Compound ………………………………….……………………….………………………...40 grams

Gross Weight………………………………………………………………………………………………………………610 grams (+/- 5%)

Activation mode(s)

- Value of Activation ……………………………………………………………………………..……6/12/24/36 V D/C 0.8 A 3-4 s

- Aerosol Generating Solid Compound activation device …………………….…Heating elements with 1.6-3.6 Ω Resistance

- Activation line supervision current (Max) ……………………………………………………………….……………………..5mA

Aerosol discharge time ………………………………………………………………………….….5 seconds (Min.) – 10 seconds (Max.)

Number of discharge nozzles………………………………………………………………………………….(4) on Top and (4) on Bottom

Generator dimension…………………………………………………………………………………..Height = 140mm, Diameter = 51mm

Self-activation temperature of Aerosol Generating Solid Compound………………………………………………………….…….300oC

Classes of Fire (NFPA 2010)

- Class A, Class B, Class C ………………………………………………………………………………………………………..Yes

- Class D and Class K….…………………………………………………………………………………………………………....No

Generator Coverage Constraints…………………………………………………..………………….Min. Ht: 0.45 m, Max area: 5.29m2

Maximum height of installation………………………………………………………………………………………………………….…..1m

Minimum Clearance (mm)

- From Persons………………………………………………………………………………………………………………….100mm

- From Combustible material………………………………………………………………………………………………….....0mm

- From generator casing ……………………………………………………………………………………………………….6.4mm

Environmental parameters

- Ozone Depletion Potential (ODP)……………………………………………………………………………………...………..Zero

- Global Warming Potential (GWP)………………………………………………………………………………………………..Zero

- Atmospheric Life Time (ALT)……………………………………………………………………………………….…….Negligible

Technical Parameters

- Electrical Conductivity…………………………………………………………………………………………..……Nil up to 75KV

- Oxygen Depletion After discharge…………………………………………………………………………………..…….Negligible

Transportation Classification

- Class 9

- UN Identification: 3335 (Air) & 3077 (Ocean)

- Packaging Group: PGIII

- Shipping Guidelines for maximum weight:

- Ground: None, Ocean: None, Cargo Air: 400 kg (881 lbs.), Passenger Air: 30 kg (66 lbs.)

# Text boxes

Discharge Nozzles at Top

SPECIFICATION DATA SHEET

AEROSOL FIRE EXTINGUISHER, 200 GRAMS

P/N TFC14-0060-1

Discharge Nozzles at Bottom